## Slide 1
WEEK 4 · SESSION 1
Architecture / Information View
Session 1: Views, functions and allocation
Today: architecture and its description, functions, allocation
Session 2: the information view, evaluation and the Lab L4 launch
Your Team Record grows: views, functions, allocation, information view

## Slide 2
Figure. Three pieces of information an AeroLink dispatch decision needs, each produced somewhere else. (FICTIONAL)
The driving question: who decides that an aircraft may fly?
SCENARIO (FICTIONAL)
An AeroLink aircraft is ready on a hub pad. A passenger party is boarding.
Who makes the release decision?
Where is the fault status, the charge state and the forecast produced?
What carries each one to the decision?

## Slide 3
Figure. Week 4 takes the needs, requirements, scenarios and the trade decision, and feeds the interfaces, the roadmap and the Phase II models.
Sources: R13 p.557; R13 p.561
Where Week 4 sits: from requirements to the first how
In: concerns, needs, scenarios, capabilities, requirements
In: the Week 3 decision, risks and TPMs
Requirements form the basis of architecture
Out: Week 5 interfaces, Week 6 roadmap, Weeks 10–11 models

## Slide 4
Figure. The description is what can be seen and reviewed; the architecture is the conception it describes.
Sources: R39t p.1445; R19 p.569
What an architecture is
ARCHITECTURE
Fundamental concepts or properties of a system in its environment embodied in its elements, relationships, and in the principles of its design and evolution
R39t · SEBoK v2.14 (2026), "Architecture (glossary)", p.1445
Conceptual; realized through a description
A description justifies what it includes and excludes

## Slide 5
Figure. A system has an architecture; a description communicates it through views and models; a framework sets requirements for the description.
Sources: R62 p.342; R19 p.569; R19 p.570; R20a p.582
How a description is organized, and why documents drift
A description consists of views and models
A framework sets requirements for the description
Separate documents need manual synchronization
A model can be one authoritative source of truth

## Slide 6
Sources: R62 p.341; R39u p.1446; R39v p.1677; R39w p.1678; R20b p.593
Framework, model, view, viewpoint: the words, and a gap
Term | MITRE | SEBoK glossary
Framework | Minimum practices and requirements for artifacts | Conventions and practices for describing architectures
View | Partial expression from a perspective | Representation from a viewpoint’s perspective
Viewpoint | Representations covering a stakeholder’s issues | Rules for constructing a view for stakeholder concerns
Paraphrased; the source wording is in the notes and the lesson.

## Slide 7
Figure. From a stakeholder to the model elements a view shows, with one AeroLink example at every link. (FICTIONAL)
Sources: R62 p.342; R62 p.344; R04 p.275; R19 p.573
Choosing views: purpose is paramount
Views directly relevant to stakeholders’ concerns
Generate only the views the purpose needs
Each view helps a stakeholder conclude objectives will be met
Course minimum: operational, functional, physical, information, enterprise

## Slide 8
Figure. Six viewpoints answer all 17 Week 1 concerns; each states its purpose as a question. (FICTIONAL)
Sources: R62 p.344
AeroLink’s view set, chosen from concerns
6 viewpoints, each with a question
17 of 17 Week 1 concerns answered
Logical view added: supplier choice stays open
Drop the information view: one concern left without one

## Slide 9
Figure. FN-006 Charge aircraft: inputs on the left, outputs on the right, each tagged information, energy or material. (FICTIONAL)
Sources: R39x p.1510; R20b p.587; R20a p.580
What a function is
FUNCTION
A function is defined by the transformation of input flows to output flows, with defined performance
R39x · SEBoK v2.14 (2026), "Function (glossary)", p.1510
Flows: data, materials or energy
Name: verb + object, never an element

## Slide 10
Figure. SEBoK’s six minimum contents of a functional view, with the AeroLink item that meets each; modes are an open row. (FICTIONAL)
Sources: R20a p.581; R20b p.587
What a functional view must contain
Capabilities; inputs and outputs; transformation steps
Grouping into sub-functions
Variations per mode; interfaces carrying the flows
Functional: input–output; behavioral: sequence and control

## Slide 11
Figure. AeroLink’s three-level decomposition: the mission function, 7 first-level functions, 17 leaves; a fourth level is marked too deep. (FICTIONAL)
Sources: R20b p.587; R20b p.594; R20c p.597
Decomposition: how deep, and in which order
From the mission (one black box) down to leaves
Stop where a physical solution is known or imaginable
Built over iterations, not one top-down pass
Pitfalls: too deep; no scenarios; no inputs and outputs

## Slide 12
Figure. The two scenarios as a worksheet: each step with an empty box for the function the class names; a person marks a step where a human decides. The answers are in the notes and the lesson. (FICTIONAL)
Sources: R20b p.594; R48c p.145
Worked example I: walking two scenarios to find functions
Walk: Read each step; ask which transformation it needs
Name: Verb + object, with inputs and outputs
Reuse: A step served by an existing function adds no function
Expose: A step no function serves is a new function or a gap

## Slide 13
Figure. 15 capabilities on the left, 17 functions on the right; one capability has a disposition instead of a function. (FICTIONAL)
Sources: R20b p.592; R20c p.598; R48c p.146
Functions from capabilities: the coverage check
14 of 15 capabilities served by a function
CAP-011 is a constraint: a disposition, not a function
12 of 12 system requirements allocated
FN-013 serves planning: no requirement, by reason

## Slide 14
Figure. Three planes: FN-006 is performed by LOG-002 and allocated to PHY-003; requirements are allocated to both structural planes. (FICTIONAL)
Sources: R19 p.571; R20b p.587; R20c p.596; R20c p.597
Logical and physical: two structural views
Logical: allocated functions, no specific implementation
Physical: the specific implementation of each logical element
Requirements are allocated to both
Elements include people, procedures and facilities

## Slide 15
Figure. Eight affinity criteria for grouping and allocating functions; one card is laid on an AeroLink allocation. (FICTIONAL)
Sources: R20c p.598; R20c p.599; R20c p.600
Allocation needs a reason: SEBoK’s criteria
Same transformation, efficiency, flow type
Central or distributed control; frequency
Dependability, environment, enterprise constraints
Course rule: one sentence per allocation, resting on an ID

## Slide 16
Figure. Two wrong paths, requirement straight to a product and function straight to a technology, against the right path through a logical plane.
Sources: R20c p.602
Two allocation pitfalls
Requirements straight to a product: no logical architecture
High-level functions straight onto technologies
Right: alternate logical and physical levels

## Slide 17
Figure. Four AeroLink allocations in three lanes, each arrow labeled with its criterion; the physical lane carries the Week 3 configuration. (FICTIONAL)
Sources: R20c p.598; R20c p.599; R48c p.145
Worked example II: function → logical → physical, with the reason
Logical: Which technology-independent element performs it?
Physical: Which element implements that, in the Week 3 configuration?
Criterion: Name the affinity and the ID it rests on
Check: The physical element is one the logical element reaches

## Slide 18
Figure. DEC-002: the question, three alternatives with the chosen one ticked, the rationale and the three tests. (FICTIONAL)
Sources: R48c p.146; R20b p.591
Recording an architecture decision
Question, alternatives, choice, rationale
Tested against the needs and risks it touches
Conditions and what would reverse it
Decisions create derived requirements

## Slide 19
Figure. The physical elements tinted by owner, with the organizational agreements between owners. (FICTIONAL)
Sources: R62 p.345; R20c p.597
The enterprise view: owners and agreements
AeroLink owns 5; vertiport operators own 3
Agreements record duties; they carry no data
As-is and to-be views show migration paths
Enterprise elements: organizations, departments, teams

## Slide 20
Figure. Stakeholder requirements and requirements analysis feed architecture design; its output is the allocated baseline, with derived requirements fed back.
Sources: R48c p.144; R48c p.145; R48c p.146
The process frame: the DoD Architecture Design process
Translates requirements into alternative design solutions
Functions allocated to hardware, software, facilities and people
Derived requirements come from solution decisions
Output: the allocated baseline

## Slide 21
Exit: one function, one reason; preparation for Session 2
ONE-MINUTE PAPER
Name one function of your enterprise, verb and object, and the criterion you would use to allocate it.
Before Session 2 (about 15 min):
List three decisions your enterprise makes every day
For each: the information it needs, and where it comes from

## Slide 22
References and credits
R04 · SEBoK v2.14 (2026), “Principles of Systems Thinking”, p.275
R13 · SEBoK v2.14 (2026), “System Requirements Definition”, p.557, 561
R19 · SEBoK v2.14 (2026), “System Architecture Design Definition”, p.569–571, 573
R20a · SEBoK v2.14 (2026), “Functional Architecture”, p.580–582
R20b · SEBoK v2.14 (2026), “Logical Architecture”, p.587, 591–594
R20c · SEBoK v2.14 (2026), “Physical Architecture”, p.596–600, 602
R39t · SEBoK v2.14 (2026), “Architecture (glossary)”, p.1445
R39u · SEBoK v2.14 (2026), “Architecture Framework (glossary)”, p.1446
R39v · SEBoK v2.14 (2026), “View (glossary)”, p.1677
R39w · SEBoK v2.14 (2026), “Viewpoint (glossary)”, p.1678
R39x · SEBoK v2.14 (2026), “Function (glossary)”, p.1510
R48c · OUSD(R&E) Systems Engineering Guidebook (2021/2022), “Architecture Design Process”, p.144–146
R62 · The MITRE Systems Engineering Guide (2014), “Architectural Frameworks, Models, and Views”, p.341–342, 344–346
CREDITS AND LICENSES
SEBoK v2.14: “This material is used under a Creative Commons Attribution-NonCommercial ShareAlike 3.0 Unported License from The Trustees of the Stevens Institute of Technology.” (SEBoK, “Bkcase Wiki:Copyright”, PDF p.31). Quotations are short and cited; no SEBoK figure or table is reproduced.
OUSD(R&E) Systems Engineering Guidebook: Distribution Statement A. Approved for public release. Distribution is unlimited.
The MITRE Systems Engineering Guide: © 2014 by The MITRE Corporation. All rights reserved. Approved for public release; distribution unlimited (Case Numbers 10-4072 and 12-1089). Quoted briefly with attribution.
Figures are original drawings for this course; none redraws a figure from the sources.
AeroLink Urban Mobility is a fictional teaching case: every number, name and statement about it is a teaching value.