## Slide 1
Figure. Week 10 fills two packages of your model: the Week 2 ConOps goes into Behavior, the Week 4 architecture into Logical; Requirements was filled in Week 9. Course illustration, not SysML v2 graphical notation.
Logical / Behavioral Modeling
Session 1: Logical architecture and action flows
Today: the logical architecture and action flows
Session 2: operating states, use cases, consistency checks, the Lab L10 launch
Your output: model v0.3 of your own enterprise

## Slide 2
Figure. A dispatch decision for a hospital patient-transfer service: three guarded branches on a triage score (lines wrapped for display). Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Driving question: the flow is well formed. Does it always continue?
VOTE
A whole-number triage score arrives. Which is true?
A · The flow always continues to one of the three actions
B · For some scores no successor is possible
C · The checker rejects this file
D · It cannot be told from the text

## Slide 3
Figure. The sources of this week and the model packages they enter, with the ID prefixes that cross: SCN and CAP from the ConOps, FN, LOG and INFO from the architecture, and the placeholders of model v0.2. Course illustration, not SysML v2 graphical notation.
What Week 10 imports from Phase I
Week 2: scenarios with steps and alternates; capabilities
Week 4: functions with their items, logical elements, information items, allocations
Week 9: placeholder subjects in Logical; capability links still waiting
Same IDs throughout

## Slide 4
Figure. Two AeroLink logical elements, each with the principal physical element that will realize it (Flight Operations is also realized at the ops center): the logical view says what must be done, the physical view gives a concrete solution, allocated in Week 11. Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Sources: R20b p.587; R20c p.596; R81 p.90
Logical versus physical architecture
PURPOSE OF LOGICAL ARCHITECTURE (SEBOK)
“models and views of the functionality and behavior of the future engineered system as it should operate while in service”
R20b · SEBoK v2.14 (2026), "Logical Architecture", p.587
Physical architecture: a concrete solution that accommodates the logical one
In SysML v2 both are parts: purely logical, or physical
Week 10 models the logical view; Week 11 the physical

## Slide 5
Figure. The three views SEBoK names for a logical architecture: what is transformed, in what order and on what condition, and how often each function runs. Course illustration, not SysML v2 graphical notation.
Sources: R20b p.587–588; R20b p.590–591
Three views of a logical architecture
Functional: functions and sub-functions, with their inputs and outputs
Behavioral: scenarios of functions and operational modes
Temporal: functions classed by how often they run
An output: a trace between logical elements and system requirements

## Slide 6
Figure. Three AeroLink functions in the order a booking is served, with the item each passes to the next where one is modeled. Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Sources: R20b p.587
Functions and the items they exchange
FUNCTION (SEBOK)
“an action that transforms inputs and generates outputs, involving data, materials, and/or energies”
R20b · SEBoK v2.14 (2026), "Logical Architecture", p.587
Inputs and outputs: the items functions exchange
Deduced from requirements, or derived from a design choice
A static tree alone does not show the flows

## Slide 7
Figure. Three pitfalls and three proven practices from SEBoK’s tables for logical architecture, in short form. Course illustration, not SysML v2 graphical notation.
Sources: R20b p.594
Pitfalls and proven practices
Pitfalls: decomposing too deep; functions without inputs and outputs; a static tree only
Practices: scenarios of functions before the tree; a function “to move” and its mode “moving”
Build a scenario: control flow, then items, then triggers

## Slide 8
Figure. Logical parts in AeroLink model v0.3: a Week 9 placeholder reused as a part definition, a new part definition, and the logical architecture as part usages (excerpt). Checked: PASS. (FICTIONAL)
Sources: R70 sl.15–16; R81 p.90
Logical decomposition: part definitions and part usages
Part definition: the kind of element; part usage: the element in this architecture
Course convention: the LOG ID on the usage, inside one part logicalArchitecture
A Week 9 placeholder with the same name becomes the definition; another name is specialized

## Slide 9
Figure. A capability, a function derived from it and two #derivedFrom dependencies in AeroLink model v0.3: one from a function, one from a requirement. Checked: PASS. (FICTIONAL)
Sources: R72 sl.30; R115 p.580; R80 p.50–51
Capabilities, functions and the links Week 9 left waiting
Course convention: a capability is an action definition, a function an action usage
A function depends on its capability: a #derivedFrom dependency
A requirement traced to a capability links the same way: a derivation must end on requirements

## Slide 10
Figure. Four AeroLink system requirements and the functions they are allocated to in model v0.3, a fragment of the matrix read from the model. Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Sources: R20b p.591–592; R81 p.110
Requirements allocated to functions
SEBoK: assign system requirements to functional elements, and trace them
Each Week 4 allocation: allocate from the requirement to the function
AeroLink: 20 allocations; three system requirements not yet allocated

## Slide 11
Figure. An information item as an item definition and FN-003 as an action usage with its in and out items, in AeroLink model v0.3. Checked: PASS. (FICTIONAL)
Sources: R82 p.117; R72 sl.30; R70 sl.17
Functions as actions: parameters and items
ACTION DEFINITION (SYSML V2.1 BETA 2)
“a kind of occurrence definition … that classifies action performances”
R82 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), "7.17 Actions", p.117
Its in and out features are its parameters
Item definition: things that exist in time and space and may flow
Course convention: a function’s in and out items come from your information view

## Slide 12
Figure. A neutral example: a logical part performs a function, and an allocation states the same responsibility as a mapping. Checked: PASS.
Sources: R72 sl.41; R82 p.136; R81 p.110–111; R76 sl.106–107
Allocating functions to logical elements: perform and allocate
ALLOCATION (SYSML V2.1 BETA 2)
“a target element is responsible for realizing some or all of the intent of the source element”
R81 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), "7.11 Parts", p.110
perform in a part: that part is the performer
allocate: a mapping across structures, often made early
Course convention: perform for functions; allocate for requirements now, logical to physical in Week 11

## Slide 13
Figure. LOG-005 in AeroLink model v0.3, typed by the Week 9 placeholder, performing the functions allocated to it, and three requirement allocations. Checked: PASS. (FICTIONAL)
Sources: R72 sl.41; R81 p.110
AeroLink worked example I: the logical architecture
7 logical parts perform 17 functions
20 requirement allocations, all from Week 4
Generated from the Week 4 case; nothing retyped
PAIR, 1 MIN
Who performs dispatch, and which requirement makes that a safety question?

## Slide 14
Figure. Three links between the same two AeroLink steps: a flow transfers the plan, a succession orders the steps, a succession flow does both. Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Sources: R72 sl.30–32; R82 p.118
Ordering and transfer: successions and flows
Succession: the first completes before the second begins
Flow: transfers an item from an output to an input
Succession flow: the output is produced before the next begins consuming it

## Slide 15
Figure. Two equivalent ways to write that a precedes b, and two reading rules. Course illustration, not SysML v2 graphical notation.
Sources: R72 sl.33–34; R82 p.134–135
Shorthands: then, and decomposition
then: a succession from the lexically previous action
An action can be decomposed directly into actions
Course reading: text order alone orders nothing; successions do

## Slide 16
Figure. SCN-002 step 4 in AeroLink model v0.3: a decision with one guarded branch and else, and a merge where the alternate rejoins. Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Sources: R72 sl.35–38; R82 p.118; R82 p.135–136
Choices: conditional successions, decide and merge
Conditional succession: taken only if its guard is true
decide: exactly one successor; else when every guard is false
merge: waits for any one predecessor
A branch target is named, never declared in place

## Slide 17
Figure. The driving question’s guards on a number line, with the uncovered score marked, and a second pair of guards that can both be true. Course illustration, not SysML v2 graphical notation.
Sources: R72 sl.35; R72 sl.38; R82 p.118; R82 p.134
The semantics of choice: gaps and overlaps
Answer B: a score of 3 has no possible successor
Overlapping guards: only one successor is chosen; the model does not say which
The checker evaluates no guard: both files pass
KEY POINT
Cover every case: write else, and check each guard against its ConOps condition.

## Slide 18
Figure. The AeroLink turnaround: after the charger is connected, charging and boarding run concurrently, and the aircraft is released when both are done (course example). Checked: PASS. (FICTIONAL)
Sources: R72 sl.40; R82 p.118
Concurrency: fork and join
fork: all its successors may start
join: waits for all its predecessors
Use a fork only where the ConOps says “at the same time”

## Slide 19
Figure. Four of the item flows of SCN-002 in AeroLink model v0.3: the plan, and the passenger party through the flight. Checked: PASS. (FICTIONAL)
Sources: R72 sl.30; R72 sl.45–46; R82 p.118
Item flows between steps, and messages at the boundary
Item flow: from an out parameter of one step to an in parameter of a later step
AeroLink SCN-002: 7 item flows, computed from the functions’ items
Across an organizational boundary: send and accept; ports follow in Week 11

## Slide 20
Figure. The first part of the SCN-002 flow inside its use case in AeroLink model v0.3: guards, steps subsetting their functions, two decisions and an ending alternate. Checked: PASS. (FICTIONAL)
Sources: R72 sl.30–38; R76 sl.101
Worked example II: SCN-002 from ConOps table to action flow
Course convention: each step an action subsetting its function
Each alternate: a guarded branch where its condition becomes known, before or after its step
A rejoin: a merge before the step; an ending: done
SCN-002: 7 steps, 3 decisions, 2 merges

## Slide 21
Figure. A decision adapted from SCN-002 step 3, shown without its checker result. Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Predict: accepted or rejected?
PREDICT, 1 MIN
Will the checker accept this file?
Write: accepted or rejected
If rejected: the line, and the reason

## Slide 22
Figure. Recorded results of the course checker (release 2026-08) on 10 course files: what it rejects, and what it accepts without complaint. Course illustration, not SysML v2 graphical notation.
Sources: R72 sl.35; R82 p.136; R82 p.146
What the checker checks, and what it cannot
The predict card: rejected at the branch; a target is named, not declared
Rejected: syntax, unresolved names, a few rules
Accepted silently: gaps, forks for choices, missing or extra initial states, unreachable states, crossings written inside a region
Zero errors is necessary, never sufficient

## Slide 23
Figure. The exit card: four fields to fill for one step and one alternate of your team’s scenario, and two questions. Course illustration, not SysML v2 graphical notation.
Exit: map one step and one alternate
Pick the scenario with the most alternates from your Week 2 ConOps
For one step and one alternate: node, construct, function
Is the alternate a choice or something happening at the same time?
Does it end the scenario, or rejoin, and where?

## Slide 24
References and credits
R20b · SEBoK v2.14 (2026), “Logical Architecture”, p.587–592, 594
R20c · SEBoK v2.14 (2026), “Physical Architecture”, p.596
R70 · Seidewitz, Intro to the SysML v2 Language: Textual Notation (Release 2026-08), “Introduction to the SysML v2 Language”, sl.15–17
R72 · Seidewitz, Intro to the SysML v2 Language: Textual Notation (Release 2026-08), “Action Definition”, sl.30–38, 40–41, 45–46
R76 · Seidewitz, Intro to the SysML v2 Language: Textual Notation (Release 2026-08), “Use Case Definition”, sl.100–101, 106–107
R80 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), “7.1 Language Overview”, p.50–51
R81 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), “7.11 Parts”, p.90, 110–111
R82 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), “7.17 Actions”, p.117–118, 134–136, 145–146, 150
R115 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), “9.6 Requirement Derivation Domain Library”, p.580
CREDITS AND LICENSES
Introduction to the SysML v2 Language, Textual Notation (Release 2026-08): Copyright © 2019–2026 Model Driven Solutions, Inc. Licensed under the Creative Commons Attribution 4.0 International License (CC BY 4.0).
SEBoK v2.14: “This material is used under a Creative Commons Attribution-NonCommercial ShareAlike 3.0 Unported License from The Trustees of the Stevens Institute of Technology.” (SEBoK, “Bkcase Wiki:Copyright”, PDF p.31). Quotations are short and cited; no SEBoK figure or table is reproduced.
Figures are original drawings for this course; none redraws a figure from the sources.
AeroLink Urban Mobility is a fictional teaching case: every number, name and statement about it is a teaching value.