## Slide 1
Figure. Three drafts of the coolant connection between a pump and an engine block, from one checked file. Checked: PASS. (FICTIONAL)
Warm-up: which draft moves the coolant?
VOTE
Which drafts say that coolant moves from the pump to the engine?
A · Draft one only
B · Drafts one and two
C · Drafts one and three
D · All three: the checker accepts them

## Slide 2
Figure. What each draft says: a flow from the pump to the engine, a flow the other way, and a binding that makes two features equal. Course illustration, not SysML v2 graphical notation.
Sources: R71 sl.24; R71 sl.26; R81 p.96
Reveal: one moves it, one reverses it, one moves nothing
Answer A: only draft one moves coolant from pump to engine
Draft two: a flow from the in item to the out item
Draft three: a binding asserts equal values; it is not a transfer
All three pass the checker

## Slide 3
Figure. Two ways to model a pump connected to a tank: a logical connection, and a connection through a medium modeled as a part. Course illustration, not SysML v2 graphical notation.
Sources: R71 sl.18; R71 sl.19; R81 p.96
Connections, and the interface medium
CONNECTION DEFINITION (TRAINING DECK)
“a part definition whose usages are connections between its ends”
R71 · Seidewitz, Intro to the SysML v2 Language: Textual Notation (Release 2026-08), "Connections", sl.18
A connection usage connects two features in context
A logical connection abstracts the medium away
Or the medium is a part in between

## Slide 4
Figure. The interface definition of IF-005 in AeroLink model v0.4: two port ends, one typed by the port definition and one by its conjugate, and a flow per crossing. Checked: PASS. (FICTIONAL)
Sources: R81 p.106; R81 p.109; R71 sl.22
Interface definitions and interface usages
INTERFACE DEFINITION (SYSML V2.1 BETA 2)
“a kind of connection definition … whose ends are restricted to be port definitions”
R81 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), "7.11 Parts", p.106
An interface usage connects two compatible ports
connect a.p to b.q: dot notation to each port

## Slide 5
Figure. Flows written once in the interface definition are established wherever the interface is used: two ports, connected, with the items moving out to in. Course illustration, not SysML v2 graphical notation.
Sources: R71 sl.26; R71 sl.27; R71 sl.28; R81 p.112; R81 p.116
Flows across an interface
A flow: from an output of the source to an input of the target
Streaming: the transfer is ongoing while both act
Flows in an interface definition: established when the interface is used
Course convention: one flow per Week 5 crossing

## Slide 6
Figure. A manifold’s outer port delegates its oxygen to the regulator inside it with a binding (course example). Checked: PASS. (FICTIONAL)
Sources: R71 sl.24; R71 sl.25; R81 p.96
Binding connectors: delegation, not transfer
bind a = b: the two features have equal values in the same context
Typical use: delegate an outer port’s feature to the inner part
A feature value (= expression) is also a binding, not a default

## Slide 7
Figure. Three interface usages in AeroLink model v0.4: an information interface, an organizational one and the charging interface. Checked: PASS. (FICTIONAL)
Sources: R20c p.597; R71 sl.18
Information, physical and organizational interfaces in the model
Physical and information: an interface between two ports, with flows
Organizational: a connection between the two parts; the agreement in its doc
Course convention: nothing flows across an agreement, so no ports

## Slide 8
Figure. The AeroLink interfaces in model v0.4 by kind, and the element most of them meet at. Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Sources: R20c p.603
AeroLink worked example III: the interface set in the model
16 interfaces: 3 physical, 10 information, 3 organizational
26 ports, 24 flows
Generated from the Week 5 case; nothing retyped
PAIR, 1 MIN
Operations Center is an end of 10 interfaces. What does SEBoK’s modularity practice ask about that?

## Slide 9
Figure. An interface requirement with the interface definition as subject, allocated to the interface usage and to the function that realizes it (course example). Checked: PASS. (FICTIONAL)
Sources: R13 p.563; R57 p.411
Interface requirements in the model
INTERFACE REQUIREMENT (SEBOK)
“a functional requirement that deals with an interaction of a system across an interface boundary with another system”
R13 · SEBoK v2.14 (2026), "System Requirements Definition", p.563
Interface management takes them as inputs, gives specifications as outputs
Course convention: one Week 9 did not model gets the interface definition as subject

## Slide 10
Figure. The three interface requirements Week 10 deferred, allocated in AeroLink model v0.4 to their interfaces and to the functions Week 10 named. Checked: PASS. (FICTIONAL)
Sources: R81 p.110; R20c p.601
Allocating interface requirements: the open items close
Each interface requirement: allocate to its interface, and to its function
AeroLink: REQ-SYS-013, REQ-SYS-014, REQ-SYS-015 now allocated
Still open: REQ-STK-021, with its reason and owner
A gap with a disposition is honest

## Slide 11
Figure. The charging systems’ design value and the satisfy claim for the charge-time requirement in AeroLink model v0.4, with its basis. Checked: PASS. (FICTIONAL)
Sources: R83 p.162; R83 p.168
Satisfy claims: the design asserts it meets a requirement
satisfy R by e: R holds with e bound to its subject
e must be of the subject’s type
The design value is an attribute of e; the basis says where it comes from
A claim, verified in Week 12

## Slide 12
Figure. A requirement on a compressor and a satisfy claim in a workshop, shown without its checker result. Course illustration, not SysML v2 graphical notation. (FICTIONAL)
Predict: what does the checker say?
PREDICT, 1 MIN
Accepted silently, accepted with a warning, or rejected?
Write your choice
And: is the claim about the right element?

## Slide 13
Figure. Recorded results of the course checker (release 2026-08) on the week’s 10 calibration files: rejected, and accepted silently or with only a warning. Course illustration, not SysML v2 graphical notation.
Sources: R83 p.162; R81 p.106
What the checker checks this week, and what it cannot
The predict card: accepted, with a warning only
Rejected: ends that are not ports, names that do not resolve
Accepted: mismatched ports, reversed flows, bindings for transfers
A warning is a finding until explained

## Slide 14
Figure. Six common errors in first physical and interface models, each with the check that catches it. Course illustration, not SysML v2 graphical notation.
Sources: R81 p.93; R71 sl.24
Common errors in physical and interface models
Both ends the same port type; a flow the wrong way
A binding where a transfer is meant
An interface the Week 5 table does not have
An allocation with no nested functions; satisfy on the wrong element

## Slide 15
Figure. The interface review checklist (course convention): the eight checks your team records in the lab, each met or a finding. Course illustration, not SysML v2 graphical notation.
Sources: R20c p.601; R81 p.93
The interface review checklist
Course convention: eight checks against Week 5 and the model
Each: met, or a finding with a note
The tool gives evidence; the judgment is yours

## Slide 16
Figure. The course mapping for Week 11, short form: each Phase I element of the Week 4 and Week 5 package and the model element it becomes. Course illustration, not SysML v2 graphical notation.
From your package to model v0.4
Course convention: generated from your Week 10 model and Week 5 export
You decide: placeholder links, placements of new functions, what crosses and which way, the functions of each interface requirement, the satisfy claims
Every ID kept; new ones continue after the highest

## Slide 17
Figure. What Week 12 does with the physical architecture and interfaces modeled this week. Course illustration, not SysML v2 graphical notation.
Bridge: Week 12, digital thread and verification
Each satisfy claim: a verification case plans its evidence
Each interface requirement: a method and a case
The digital thread: need to requirement to design to verification

## Slide 18
Figure. Lab L11 deliverables: three files, one upload (course convention). Course illustration, not SysML v2 graphical notation.
Lab L11: model v0.4 of your enterprise
Due before Week 12, Session 1, on the LMS; your own enterprise, never AeroLink
Your own enterprise, never AeroLink
Three files: team-NN-model-v04.sysml, team-NN-interface-review.md, team-NN-checker-log.txt
Zero checker errors; every warning explained
Formative feedback before Week 12, Session 2

## Slide 19
Figure. In class: import, link and place, set the crossings, preview the ports in the lab tool. Course illustration, not SysML v2 graphical notation.
Team work: what crosses your interfaces
12 minutes, in teams, in the Week 11 lab tool
Import your Week 10 model and your Week 5 export
Link each Week 8 or 9 part definition; place Week 10’s new functions
Each interface: every crossing as an item, with its direction
Preview the ports and flows

## Slide 20
Instructor checkpoint
Per team: one interface, its port definition, one direction
Show: one interface and its crossings
Show: the port definition and which end is conjugate
Justify one direction from Week 4
Note one fix to make before day 2

## Slide 21
Figure. A suggested seven-day plan for Lab L11, with the lead role for each task (course convention). Course illustration, not SysML v2 graphical notation.
Close: the next seven days
Quiz Q11 and the applied exercise open today. Log your hours.

## Slide 22
References and credits
R13 · SEBoK v2.14 (2026), “System Requirements Definition”, p.563
R20c · SEBoK v2.14 (2026), “Physical Architecture”, p.596–603
R57 · The MITRE Systems Engineering Guide (2014), “Interface Management”, p.411
R71 · Seidewitz, Intro to the SysML v2 Language: Textual Notation (Release 2026-08), “Connections”, sl.18–22, 24–28
R81 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), “7.11 Parts”, p.90, 93, 95–96, 106, 109–112, 116
R83 · OMG SysML v2.1 Beta 2, Part 1 (Release 2026-07), “7.21 Requirements”, p.162, 168
CREDITS AND LICENSES
Introduction to the SysML v2 Language, Textual Notation (Release 2026-08): Copyright © 2019–2026 Model Driven Solutions, Inc. Licensed under the Creative Commons Attribution 4.0 International License (CC BY 4.0).
SEBoK v2.14: “This material is used under a Creative Commons Attribution-NonCommercial ShareAlike 3.0 Unported License from The Trustees of the Stevens Institute of Technology.” (SEBoK, “Bkcase Wiki:Copyright”, PDF p.31). Quotations are short and cited; no SEBoK figure or table is reproduced.
The MITRE Systems Engineering Guide: © 2014 by The MITRE Corporation. All rights reserved. Approved for public release; distribution unlimited (Case Numbers 10-4072 and 12-1089). Quoted briefly with attribution.
Figures are original drawings for this course; none redraws a figure from the sources.
AeroLink Urban Mobility is a fictional teaching case: every number, name and statement about it is a teaching value.